## Slide 1: Introduction to Petrochemical Processes
Ref. 1: U. R. Chaudhuri, Fundamentals of Petroleum and Petrochemical Engineering, CRC Press, 2011, Chapter 5.
Ref. 2: Ante Jukić, Lecture notes: Production of Olefins, University of Zagreb.

## Slide 2: DEFINTIONS OF PETROCHEMICALS
Petrochemicals are chemicals derived from petroleum products. Examples of petrochemicals are plastics, rubbers, fibers, paints, solvents, and detergents.
Petroleum products maybe grouped as (1) feedstocks (first-generation petrochemicals), (2) intermediates (second-generation petrochemicals), and (3) finished products (third-generation petrochemicals).
Products similar to petrochemicals derived from non-petroleum sources are not strictly petrochemicals. For example, cellulose, natural rubber, natural resins, and ethanol of plant origin are strictly non-petrochemicals.
Coal distillation is also a source of varieties of coal chemicals, e.g., benzene, toluene, xylene, and naphthalene.

## Slide 3: DEFINTIONS OF PETROCHEMICALS
Non-hydrocarbons obtained from petroleum, e.g., hydrogen, carbon monoxide, carbon dioxide, sulfur, and carbon, are also loosely called petrochemicals.
Hydrogen, nitrogen and oxides of carbon manufactured from steam reforming of natural gas and partial oxidation of naphtha are also petrochemicals. These are used for production of methanol, ammonia, urea, melamine, fertilizer, etc.
Feedstocks are the raw hydrocarbons obtained from crude oil refining by distillation
and thermal and catalytic processes.
Natural gas and naphtha (from atmospheric distillation of crude oil), are
the major raw materials for the manufacture of second-generation petrochemicals.

## Slide 4: DEFINTIONS OF PETROCHEMICALS
Similarly, benzene, toluene, and xylenes, obtained by catalytic reforming and catalytic cracking processes, are another raw materials for the manufacture of second-generation petrochemicals.
Benzene, toluene, xylene, and heavier aromatics are also generated as by-products
from petrochemical plants. Thus, the feedstocks for petrochemical plants are either
directly obtained from refineries or are further processed to generate them in the
petrochemical plant itself.
A list of the major petrochemicals is given in the following Table.

## Slide 6: DEFINTIONS OF PETROCHEMICALS
INTERMEDIATES
Thermal cracking of ethane, propane, butane, and naphtha produces cracked gases or
olefins (ethylene, propylene, butylenes, acetylene, etc.) and liquids (benzene, toluene,
xylene, etc.).
Olefins are the starting material (monomers) for polyolefin plants. Olefins
are also reacted with other hydrocarbons or non-hydrocarbon chemicals to generate
vinyl chloride, ethylene glycol, ethylene oxide, etc., and these are used as
the starting materials (monomers) for the manufacture of a variety of polymers.

## Slide 7: DEFINTIONS OF PETROCHEMICALS
FINISHED PRODUCTS
Using the above intermediates, a variety of plastics, rubber, fibre, solvent, paint, etc.,
are manufactured. Polymerization reactions are carried out for these monomers or
intermediates to various polymers, resinous and liquid products.
A large number of unit operations and processes are involved in a petrochemical
plant. Since catalysts play a major role in the synthesis of petrochemicals, research and
development of new catalysts is a continuous endeavor by the manufacturers. The reactors used are tubular, stirred tank or kettle type. These may be packed bed or fluidized bed types, Both single and multiple numbers of reactors are used

## Slide 8: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
Pyrolysis of hydrocarbons is the most important process of petrochemical production
It presents the main source for the majority of basic organic industrial raw materials:
α-olefin (ethene, propene, isobutene, butene), butadiene and aromatic hydrocarbons (BTX = benzene, toluene, xylene).
Pyrolysis is non-catalyzed process of thermal decomposition of hydrocarbons.
It is performed at very high temperatures, 750 - 900 °C, and approximately normal pressure.
Olefinic and aromatic hydrocarbons are the starting materials for the vast majority of
(about 75%) organic chemical products. Therefore, pyrolysis of hydrocarbons is a
basic process of petrochemical and organic chemical industry.
.

## Slide 9: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
The highest yield of ethylene is obtained by the dehydrogenation (pyrolysis) of ethane (80%), but due to insufficient quantity, the other raw materials in the production of olefins usually are: naphtha, propane-butane mixture (LPG), gas oil and natural gas condensate
Raw material for steam cracking of hydrocarbons (2002), wt%
 | Europe | Japan | USA | World
Refinery gas | 9 | 2 | 3 | 17
Ethane, LPG | 10 | -- | 52 | 27
Naphtha | 70 | 98 | 21 | 48
Gas Oil | 11 | 0 | 24 | 8

## Slide 10: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
Due to the larger availability of naphtha as compared to gases, naphtha cracking is widely accepted for the manufacture of olefins. Naphtha is a mixture of hydrocarbons boiling in the range of the lowest boiling component (C5) to 150°C.
A suitable boiling range for feedstock naphtha for olefin production is below 100°C and should have a paraffin content of more than 75%.
Usually, naphtha in the boiling range of 90°C−150°C is catalytically reformed in a refinery either to produce gasoline or aromatics. Hence, in the refinery, C5−90°C cut is separated in the distillation unit and is sold to the petrochemical industry.

## Slide 11: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
Mainly, cracking reactions of one or more covalent C-C bonds of the hydrocarbon
molecules take place, by a free radical mechanism. Consequently, a larger number of smaller molecules is formed. At the same time, reaction of dehydrogenation is going on, by cracking the C-H bonds. Both reactions lead to α-olefins formation, the basic products of the process.

## Slide 12: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
If the reaction is continued indefinitely, branched and cyclized heavy hydrocarbons will be produced and coke will be generated as the ultimate product.
Therefore, the cracking reaction is carried out in a very short residence time, i.e., the feed passes the heater tubes at very high speed to avoid undesirable heavy end products and coke. Usually, residence time is maintained at <1 sec in the traditional cracker furnaces and it is of the order of a few milliseconds in the modern millisecond furnaces.
Since a coke layer develops inside the tube surface, the heat transfer rate is rapidly reduced, causing reduced cracking and poor olefins yield. Steam is introduced with the feed to remove the coke layer on the tube surface by converting coke into carbon monoxide and hydrogen by water gas reaction: C + H2O(steam) = CO + H2

## Slide 13: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
However, coke cannot be removed completely by steam and the thickness grows during the operating period of the furnace.
When the coke layer reaches the point at which cracking operation shows poor yield, the furnace is taken out of service and decoking is carried out with air and steam to remove coke to the maximum extent.
Thus, a cracker furnace operates cyclically between the cracking and decoking operations (cyclic time is about 20 days).
Excess steam may also partially convert some of the hydrocarbons or naphtha components to carbon monoxide and hydrogen and reduce the yield of olefins.

## Slide 14: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
Pyrolysis (steam cracking) of hydrocarbons results with the following products:
ethylene CH2=CH2
propylene CH2=CH−CH3
1-butene CH2=CH−CH2−CH3
2-butene CH3−CH=CH−CH3
isobutene CH2=C(CH3)2
butadiene CH2=CH−CH=CH2
hydrogen H2
methane CH4
pyrolysis gasoline C5 +
Note: Other paraffinic products such as ethane, propane and butanes are separated and recycled to the reactor.

## Slide 15: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
Schematic representation of the pyrolysis of hydrocarbons with steam:

## Slide 16: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
The products obtained in the pyrolysis reactor depend on the composition of the feed, the hydrocarbon-to-steam ratio, and on the cracking temperature and furnace residence time.
Typical product yields (wt%) from pyrolysis of various hydrocarbon feedstocks
Feedstock | Ethane | Propane | Naphtha | Gas Oil
Product |  |  |  | 
Hydrogen | 5 | 2 | 1 | 1
Methane | 9 | 27 | 15 | 8
Ethene | 78 | 42 | 25-35 | 15-23
Propene | 3 | 19 | 16 | 14
Butenes | --- | --- | 5 | 5
Butadiene | 2 | 3 | 5 | 6
PG | 3 | 7 | 19-29 | 20
Fuel Oil | -- | -- | 4 | 23-31

## Slide 17: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
The steam cracking units have two main sections:
Pyrolysis reactor
- Tubular reactor (furnace)
- Fluidized-bed reactor
Separation section
- Stabilizer
- H2S/CO2 Absorber
- H2 Flash Drum
- De-methanizer, De-ethanizer, De-propanizer, De-butanizer
- Ethylene Separator, Propylene Separator, Butylene Separator

## Slide 18: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
The most common pyrolysis reactor for lower hydrocarbon feeds (ethane, LPG, Naptha) is the tubular reactor (it is called pyrolysis furnace).

## Slide 19: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)

## Slide 20: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)
1. Naphtha vapor flows through the inside of the tubes in the furnace
2. Rows of furnace guns which burn methane to generate heat inside the furnace
3. A peephole (eyehole)

## Slide 21: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)

## Slide 22: Production of Olefins Steam Cracking of Hydrocarbons (pyrolysis)

## Slide 23
1 - pyrolysis reactor (furnace), 2 - cooling tube heat exchanger, 3 - steam generator, 4 – primary fractionator, 5 - cooling distillation column, 6 - gas cleaning, 7 - the drying column, 8 - low temperature cooling, 9 - separation of methane and hydrogen, 10 – column for de-methanizer, 11 – column for de-ethanizer, 12 - hydrogenation of acetylene,13 - separation of ethylene, 14 – column for de-propanizer, 15 - hydrogenation of methylacetylene, 16 - the separation of propylene, 17 - columns for de-butanizer, 18 - columns for de-penthanizer, 19 - separation of pyrolysis gasoline